SYS-001-001
WHT Sensor User Requirements
# Introduction
## Purpose
This document describes the tasks that the users must be able to accomplish with the WHT Sensor system (referred as “WHT Sensor” in the next sections).
## Scope
The WHT Sensor aims to provide do-it-yourself indoor temperature and relative humidity measurements without the need of network cables or a power outlet.
## References
(None).
## Overview of Document
After a small description of the different roles, each task (one per section) will be described from the users’ point of view with their goals and benefits.
# User Requirements
As WHT Sensor aims to be a do-it-yourself product, only one role was identified: the User. He would typically buy, configure and maintain the WHT Sensor himself.
## Monitor Room Temperature
As a User, I want my WHT Sensor to monitor the temperature of a room with:
- the same accuracy (or better) as my thermostat (±0.5 °C); and
- the same frequency (or faster) than the data provided with my electricity bills (1 measurement per hour);
so I can easily analyze them together and estimate the thermal efficiency of my house.
## Monitor Room Relative Humidity
As a User, I would like my WHT Sensor to monitor the relative humidity of a room with:
- a maximum accuracy of ±5%); and
- the same frequency as the temperature measurements;
so I may compute the apparent temperature or monitor the room confort.
## Receive MQTT Message
As a User, I want my WHT Sensor to publish messages to the following topics on my MQTT server:
- “sensors/<room>/T”, for the temperature measurements in °C;
- “sensors/<room>/RH”, for the relative humidity in %.
Where <room> and the MQTT server URL can be configured on each Sensor.
## Put Sensor Everywhere
As a User, I want my WHT Sensor to be wireless so I can deploy it wherever I want in my house without pulling cables around and without the need to changes batteries for at least 6 months.
## DIY
As a User, I want to be able to make my own WHT Sensor from common Arduino modules; available at Adafruit or Sparkfun for example; as they are easily accessible and I most probably already own some of them.
## Spare Hobby Budget
As a User, one WHT Sensor shall cost less than 15 $ if I build it myself; without counting my time; so the expenses can fit in the budget for my hobbies.